## Slide 1: CPE 323 Introduction to Embedded Computer Systems: The MSP430 Serial Communication
Instructor: Dr Aleksandar Milenkovic Lecture Notes

## Slide 2: Communication
Internet of things
  Cars, Appliances (e.g. refrigerator) …
Workstation and development board
  Inter board comm. (several feet)
On-board
  Inter-chip comm. (several millimeters)

## Slide 3: Inter-chip Communication
Parallel vs. Serial
  Metrics: Cost, Bandwidth, Latency
Types of communication
  Duplex
  Half-duplex
  Simplex
Handshaking
  RDY (ready data)
  ACK (acknowledge data)

## Slide 4: Handshaking Example
Simplex communication (from A to B)
Handshaking in time
  A: set data
  A: set Rdy
  B: get data
  B: set Ack
  A: de-assert Rdy, Data
  B: de-assert Ack
A
B
Data(7:0)
Rdy
Ack
Rdy
Ack
Data

## Slide 5: Serial Communication
Common types of serial communication
  Asynchronous serial communication (UART – Universal Asynchronous Receiver/Transmitter)
  Serial Peripheral Interface (SPI)
  Inter-integrated circuit (I2C) bus

## Slide 6: MSP430xG461x Microcontroller

## Slide 7: MSP430xF20x3 Microcontroller

## Slide 8: MSP430 Comm. Peripherals
Universal Serial Interface (USI)
  Small module (F20x2, F20x3 devices)
  SPI and I2C (needs some help from SW)
Universal Serial Communication Interface (USCI)
  Contains two channels USCI_A, USCI_B
  USCI_A: UART, IrDA, SPI
  USCI_B: SPI, I2C
Universal Synchronous/Asynchronous Receiver/Transmitter (USART)
  UART, SPI (and I2C in some devices)

## Slide 9: Asynchronous Serial Communication
Popular in embedded systems (uart)
Single wire for each direction (RxD, TxD) and common ground (Gnd)
Duplex link (data can be sent simultaneously in both directions)
A
B
RxD
RxD
TxD
TxD
Gnd

## Slide 10: Asynchronous Serial Interface
Asynchronous
  Transmitted and received data are not synchronized over any extended period
  No synchronization between receiver and transmitter clocks
Serial
  Usually character oriented
  Data stream divided into individual bits at the transmitter side
  Individual bits are grouped into characters at the receiving side
Information is usually transmitted as ASCII-encoded characters
  7 or 8 bits of information plus control bits

## Slide 11: How does it work? Transmitter (device T) – wants to send a byte to receiver (device R)
1. Microcontroller (T side): Writes the byte into the Transmit Data Buffer (visible to the programmer) of the Serial I/O interface
2. Serial I/O interface (T side): Loads the data from the Data Transmit Buffer into a shift register (parallel-in/serial-out); The data are shifted out of this register using Tclock clock signal.
3. Serial I/O interface (R side): The data from a single transmission line that goes from device T to device R are shifted in the serial-in/parallel out shift register. The data are shifted on every Rclock cycle. It is assumed that Tclock=Rclock
4. Serial I/O interface (R side): When all 8 bits are received by in the shift register, the data is transferred to the Receive Data Buffer in parallel.
5. Microcontroller (R side): Reads the byte from the Receive Data Buffer (visible to the programmer) of the Serial I/O interface.

## Slide 12: Format of Data
Data are sent in relatively short frames (typically 1 byte)
Logic levels: Logic one – MARK, Logic zero – SPACE
If nothing to transmit, the transmitter holds the MARK level
Start bit: to mark the beginning of a new character, the line changes from the mark to the space level for one bit time. This synchronizes the transmitter and receiver. When the receiver detects the start bit, it knows to start clocking in the serial data bits.
Data bits: any number of bits can be theoretically sent. In practice, it is between 5 and 8 bits.
Parity bit: 7 bits are needed to encode a character. Most UARTS allow 8 bits to be sent. The parity bit is added to the data to make the total of ones odd (ODD parity) or even (EVEN parity). The parity bit is used to detect possible errors in the data stream.
Stop bit: The stop bit is added at the end of the data bits. This gives at least one bit time period between successive characters. Some systems require 2 or more stop bits.

## Slide 13: Format of Data
Line idles high (MARK)
Character format
  ST: Start bit (low, SPACE)
  7, 8 data bits (D0-D7), LSB goes first
  SP: one stop bit (high, MARK)
Baud rate: bits/sec

## Slide 14: How does asynchronous comm. work?
Transmitter and receiver run independently (no clock is shared)
How do we synchronize them?
Clock at the receiver side must run faster than the baud rate (e.g., 16x)
Basic procedure for receiving a frame
  1. When falling edge of ST bit is detected, the receiver clock samples the input line half-way through the bit (be sure that is true ST bit)
  2. Sample the input after a half bit period to confirm the valid start bit
  3. Sample the input after the next bit period (lsb bit)
  4. Repeat this until all 8 bits are received
  5. Wait a further bit period and check that the input is high as expected (SP bit). Indicate a framing error if no valid stop bit is detected.

## Slide 15: USCI in UART mode
7- or 8-bit data with odd, even, or non-parity
Independent transmit and receive shift registers
Separate transmit and receive buffer registers
LSB-first or MSB-first data transmit and receive
Built-in idle-line and address-bit communication protocols for multiprocessor systems
Receiver start-edge detection for auto-wake up from LPMx modes
Programmable baud rate with modulation for fractional baud rate support
Status flags for error detection and suppression
Status flags for address detection
Independent interrupt capability for receive and transmit

## Slide 16: USCI Block Diagram

## Slide 17: USCI Initialization Process
1) Set UCSWRST
  (BIS.B #UCSWRST,&UCAxCTL1)
2) Initialize all USCI registers with UCSWRST = 1 (including UCAxCTL1)
3) Configure ports
4) Clear UCSWRST via software
  (BIC.B #UCSWRST,&UCAxCTL1)
5) Enable interrupts (optional) via UCAxRXIE and/or UCAxTXIE

## Slide 18: USCI Registers: UART mode

## Slide 19: Receive Error Conditions

## Slide 20: Echo a Character Using USCI
#include <msp430xG46x.h>
void main(void)
{
volatile unsigned int i;
WDTCTL = WDTPW+WDTHOLD; // Stop WDT
P2SEL |= BIT4 + BIT5; // P4.7,6 = USCI_A0 RXD/TXD
UCA0CTL1 |= UCSSEL_2; // SMCLK
UCA0BR0 = 0x09; // 1MHz 115200
UCA0BR1 = 0x00; // 1MHz 115200
UCA0MCTL = 0x01; // Modulation
UCA0CTL1 &= ~UCSWRST; // **Initialize USCI state machine**
IE2 |= UCA0RXIE; // Enable USCI_A0 RX interrupt
_BIS_SR(LPM0_bits + GIE); // Enter LPM0, interrupts enabled
}
// Echo back RXed character, confirm TX buffer is ready first
#pragma vector=USCIAB0RX_VECTOR
__interrupt void USCIA0RX_ISR (void)
{
while(!(IFG2&UCA0TXIFG));
UCA0TXBUF = UCA0RXBUF; // TX -> RXed character
}

## Slide 21: USCI_A Configuration
UXA0CTL0
  UCSYNC = 0 (async. mode)
  UCMODExx
    00 – standard UART mode
    01 or 10 – multiprocessor modes
    11- automatic baud rate detection (LIN)
Baud rate setting
  BRCLK – the input clock (ACLK, SMCLK, UCLK)
  BITCLK – fBITCLK = fBaud
  BITCLK16 – fBITCLK16 = 16*fBITCLK
Challenge: BITCLK is rarely close to being perfect factor of BRCLK

## Slide 22: USCI_A Configuration: Baud Rate
Oversampling mode, UCOS16 = 1
  BRCLK is first divided to give BITCLK16, which is further divided by a factor of 16 to get BITCLK
Low frequency mode, UCOS16 = 0
  BRCLK if used directly as the sampling clock and is divided to give BITCLK
BRCLK division
  UCA0BR0 and UCA0BR1: provides main divider
  UCBRFx: modulates the divider that gives BITCLK16 in oversampling mode
  UCBRSx: modulates the divider that gives BITCLK

## Slide 23: Oversampling Mode (UCOS16=1)
fbaud = 9600 Hz, fBRCLK = 220 (1,048,576 Hz)
fBIT16CLK = 16* fbaud = 153.6 KHz
Divider: 220 /153,600 = 6.83 (?)
  Use closest integer: round down to 6
    => 1,048,576 Hz / 6 ~ 10,922 (not 9,600)
  One bit period: 6.83 * 16 = 109.2 BRCLK cycles
  Modulate: some periods will be 6, some will be 7 BRCLK
  x*6 + (16-x)*7 = 109.2 => x=3
    13 BITCLK16 cycles have length of 7 BRCLK
    3 BITCLK16 cycles have length of 6 BRCLK

## Slide 24: Typical Baud Rates (UCSO16=1)

## Slide 25: Low-frequency Mode (UCOS16=0)
Supports baud rates from low frequency clock sources
  E.g. 9600 baud from a 32768Hz crystal
fBRCLK < 16*fbaud (UCOS16 = 0)
E.g., ACLK = 32768 Hz, fbaud = 9,600
fBRCLK / fbaud = 3.41 => cannot make the length of each BITCLK correct
Nint(8* fBRCLK / fbaud ) = (8 – UCBRSx)*UCBRx + UCBRSx*(UCBRx+1)
  5 bits with duration 3 BRCLK, 3 bits with duration of 4 BRCLK (~3.4 avg)

## Slide 26: Typical Baud Rates

## Slide 27: UCAxCTL0

## Slide 28: UCAxCTL1

## Slide 29: UCAxBRx

## Slide 30: Interface Standards
UART mode for on-board communication
  Logic levels: VSS (logic 0), VCC (logic 1)
  Devices share ground and power supply
Communication between separate devices (e.g., dev. board and PC)
  Need a standard interface (e.g. RS232)
  Defines logic levels, connector types, …
External circuits are needed to connect MSP430 to an RS-232 port (e.g. MAX3221 + charge pumps that make ± 2*VCC)

## Slide 31: RS-232 Interface Standard
Bi-polar:
  +3 to +12V (ON, 0-state, or SPACE condition)
  -3 to –12V (OFF, 1-state, or MARK condition)
Modern computers accept 0V as MARK
“Dead area” between –3V and 3V is designed to absorb line noise
Originally developed as a standard for communication between computer equipment and modems
From the point of view of this standard:
  MODEM: data communications equipment (DCE)
  Computer equipment: data terminal equipment (DTE)
Therefore, RS-232C was intended for DTE-DCE links (not for DTE-DTE links, as it is frequently used now)

## Slide 32: RS-232 Interface Standard
Each manufacturer may choose to implement only a subset of functions defined by this standard
Two widely used connectors: DB-9 and DB-25
Three types of link
  Simplex
  Half-duplex
  Full-duplex
Basic control signals
  RTS (Request to send): DTE indicates to the DCE that it wants to send data
  CTS (Clear to send): DCE indicates that it is ready to receive data
  DSR (Data set ready): indication from the DCE (i.e., the modem) that it is on
  DTR (Data terminal ready): indication from the DTE that it is on

## Slide 33: RS-232 Interface Standard, another example

## Slide 34: RS-232 Interface Standard
Let’s take a look at DB-9

## Slide 35: RS-232 Interface Standard Example: 9 to 25 pin cable layout for asynchronous data

## Slide 36: The Minimal RS-232 Function
7
2
7
2
DTE
DCE
DTE to DCE in simplex mode
7
2
7
3
DTE
DTE
DTE to DTE in simplex mode

## Slide 37: The Minimal RS-232 Function
7
2
7
2
DTE
DCE
DTE to DCE in full-duplex mode
3
3
7
2
7
3
DTE
DTE
DTE to DTE in full-duplex mode
3
2

## Slide 38: The Minimal RS-232 Function
7
2
DTE
DCE
DTE to DCE with remote control
3
4
5
TxD
RxD
RTS
CTS
7
2
3
4
5
RxD
TxD
CTS
RTS
7
2
DTE
DTE
DTE to DTE with remote control
3
4
5
TxD
RxD
RTS
CTS
7
2
3
4
5
TxD
RxD
RTS
CTS

## Slide 39: Handshaking Between RTS and CTS

## Slide 40: Null Modem
Null-modem simulates a DTE-DCE-DCE-DTE circuit

## Slide 41: USART Peripheral Interface
Universal Synchronous/Asynchronous Receive/Transmit (USART) peripheral interface supports two modes
  Asynchronous UART mode (User manual, Ch. 17)
  Synchronous Peripheral Interface, SPI mode (User manual, Ch. 18)
UART mode:
  Transmit/receive characters at a bit rate asynchronous to another device
  Connects to an external system via two external pins URXD and UTXD (P3.4, P3.5)
  Timing is based on selected baud rate (both transmit and receive use the same baud rate)

## Slide 42: UART Features
7- or 8-bit data width; odd, even, or non-parity
Independent transmit and receive shift reg.
Separate transmit and receive buffer registers
LSB-first data transmit and receive
Built-in idle-line and address-bit communication protocols for multiprocessor systems
Receiver start-edge detection for auto-wake up from LPMx modes
Programmable baud rate with modulation for fractional baud rate support
Status flags for error detection
Independent interrupt capability for transmit and receive

## Slide 43: USART Block Diagram: UART mode

## Slide 44: Initialization Sequence & Character Format
Initialization Sequence
  1) Set SWRST (BIS.B #SWRST,&UxCTL)
  2) Initialize all USART registers with SWRST = 1 (including UxCTL)
  3) Enable USART module via the MEx SFRs (URXEx and/or UTXEx)
  4) Clear SWRST via software (BIC.B #SWRST,&UxCTL)
  5) Enable interrupts (optional) via the IEx SFRs (URXIEx and/or UTXIEx)
  Note: Failure to follow this process may result in unpredictable USART behavior.
Character format

## Slide 45: USART Interrupt Vectors
The USART has one interrupt vector for transmission and one interrupt vector for reception
Transmit:
  The UTXIFGx interrupt flag is set by the transmitter to indicate that UxTXBUF is ready to accept another character. An interrupt request is generated if UTXIEx and GIE are also set. UTXIFGx is automatically reset if the interrupt request is serviced or if a character is written to UxTXBUF.
  UTXIFGx is set after a PUC or when SWRST = 1. UTXIEx is reset after a PUC or when SWRST = 1.
Receive:
  The URXIFGx interrupt flag is set each time a character is received and loaded into UxRXBUF. An interrupt request is generated if URXIEx and GIE are also set. URXIFGx and URXIEx are reset by a system reset PUC signal or when SWRST = 1. URXIFGx is automatically reset if the pending interrupt is served (when URXSE = 0) or when UxRXBUF is read.

## Slide 46: Control Registers

## Slide 47: C Examples, UART 2400
//******************************************************************************
// MSP-FET430P140 Demo - USART1 UART 2400 Ultra-low Power Echo ISR, 32kHz ACLK
//
// Description; Echo a received character, RX ISR used. In the Mainloop UART1
// is made ready to receive one character with interrupt active. The Mainloop
// waits in LPM3. The UART1 ISR forces the Mainloop to exit LPM3 after
// receiving one character which echo's back the received character.
// ACLK = UCLK1 = LFXT1 = 32768, MCLK = SMCLK = DCO~ 800k
// Baud rate divider with 32768hz XTAL @2400 = 32768Hz/2400 = 13.65 (000Dh)
// //*An external watch crystal is required on XIN XOUT for ACLK*//
//
// MSP430F149
// -----------------
// /|\| XIN|-
// | | | 32kHz
// --|RST XOUT|-
// | |
// | P3.6|----------->
// | | 2400 - 8N1
// | P3.7|<-----------
//
//
// M. Buccini
// Texas Instruments, Inc
// October 2003
// Built with IAR Embedded Workbench Version: 1.26B
// January 2004
// Updated for IAR Embedded Workbench Version: 2.21B
//******************************************************************************
#include <msp430x14x.h>
void main(void)
{
WDTCTL = WDTPW + WDTHOLD; // Stop WDT
P3SEL |= 0xC0; // P3.6,7 = USART1 option select
ME2 |= UTXE1 + URXE1; // Enable USART1 TXD/RXD
UCTL1 |= CHAR; // 8-bit character
UTCTL1 |= SSEL0; // UCLK = ACLK
UBR01 = 0x0D; // 32k/2400 - 13.65
UBR11 = 0x00;
UMCTL1 = 0x6B; // Modulation
UCTL1 &= ~SWRST; // Initialize USART state machine
IE2 |= URXIE1; // Enable USART1 RX interrupt
// Mainloop
for (;;)
{
_BIS_SR(LPM3_bits + GIE); // Enter LPM3 w/interrupt
while (!(IFG2 & UTXIFG1)); // USART1 TX buffer ready?
TXBUF1 = RXBUF1; // RXBUF1 to TXBUF1
}
}
// UART1 RX ISR will for exit from LPM3 in Mainloop
interrupt[UART1RX_VECTOR] void usart1_rx (void)
{
_BIC_SR_IRQ(LPM3_bits);// Clear LPM3 bits from 0(SR)
}

## Slide 48: CPE 323 Introduction to Embedded Computer Systems: The MSP430 Serial Peripheral Interface
Instructor: Dr Aleksandar Milenkovic Lecture Notes

## Slide 49: Serial Peripheral Interface
Serial Peripheral Interface – SPI
  It is a synchronous serial data link standard named by Motorola that operates in full duplex mode
  Devices communicate in master/slave mode where the master device initiates the data frame. Multiple slave devices are allowed with individual slave select (chip select) lines.
The SPI bus specifies four logic signals
  SCLK — Serial Clock (output from master)
  MOSI/SIMO — Master Output, Slave Input (output from master)
  MISO/SOMI — Master Input, Slave Output (output from slave)
  SS — Slave Select (active low; output from master)

## Slide 50: SPI Mode: Signal Definition
UCxSIMO Slave in, master out
  Master mode: UCxSIMO is the data output line
  Slave mode: UCxSIMO is the data input line
UCxSOMI Slave out, master in
  Master mode: UCxSOMI is the data input line
  Slave mode: UCxSOMI is the data output line
UCxCLK USCI SPI clock
  Master mode: UCxCLK is an output
  Slave mode: UCxCLK is an input
UCxSTE Slave transmit enable.
  Used in 4-pin mode to allow multiple masters on a single bus. Not used in 3-pin mode.

## Slide 51: USCI: SPI Mode

## Slide 52: SPI Mode: Initialization Sequence
1) Set UCSWRST (BIS.B #UCSWRST,&UCxCTL1)
2) Initialize all USCI registers with UCSWRST=1 (including UCxCTL1)
3) Configure ports.
4) Clear UCSWRST via software (BIC.B #UCSWRST,&UCxCTL1)
5) Enable interrupts (optional) via UCxRXIE and/or UCxTXIE

## Slide 53: SPI Master Mode
1) Move data to UCxTXBUF to initiate transfer
2) UCxTXBUF data is moved to the TX shift register when the TX shift register is empty, initiating data transfer on UCxSIMO starting with either the MSB or LSB
3) Data on UCxSOMI is shifted into the receive shift register on the opposite clock edge
4) When the character is received, the receive data is moved from the RX shift register to UCxRXBUF and the receive interrupt flag, UCxRXIFG, is set, indicating the RX/TX operation is complete
(Note #1: A set transmit interrupt flag, UCxTXIFG, indicates that data has moved from UCxTXBUF to the TX shift register and UCxTXBUF is ready for new data. It does not indicate RX/TX completion)
(Note #2: To receive data into the USCI in master mode, data must be written to UCxTXBUF because receive and transmit operations operate concurrently)

## Slide 54: 4-pin SPI Master Mode
UCxSTE is used to prevent conflicts with another master and controls the master
When UCxSTE is in the master-inactive state:
  UCxSIMO and UCxCLK are set to inputs and no longer drive the bus
  The error bit UCFE is set indicating a communication integrity violation to be handled by the user
  The internal state machines are reset and the shift operation is aborted
If data is written into UCxTXBUF while the master is held inactive by UCxSTE, it will be transmit as soon as UCxSTE transitions to the master-active state.
If an active transfer is aborted by UCxSTE transitioning to the master-inactive state, the data must be re-written into UCxTXBUF to be transferred when UCxSTE transitions back to the master-active state.

## Slide 55: SPI Slave Mode
UCxCLK is used as the input for the SPI clock and must be supplied by the external master
UCxTXBUF moved to the TX shift register before the start of UCxCLK
Transmitted on UCxSOMI.
Data on UCxSIMO is shifted into the receive shift register on the opposite edge of UCxCLK and moved to UCxRXBUF when the set number of bits are received
When data is moved from the RX shift register to UCxRXBUF, the UCxRXIFG interrupt flag is set, indicating that data has been received
(Note #1: The overrun error bit UCOE is set when the previously received data is not read from UCxRXBUF before new data is moved to UCxRXBUF).

## Slide 56: 4-pin SPI Slave Mode
In 4-pin slave mode, UCxSTE is used by the slave to enable the transmit and receive operations and is provided by the SPI master
When UCxSTE is in the slave-active state, the slave operates normally
When UCxSTE is in the slave-inactive state:
  Any receive operation in progress on UCxSIMO is halted UCxSOMI is set to the input direction
  The shift operation is halted until the UCxSTE line transitions into the slave transmit active state

## Slide 57: SPI Mode
When the USCI module is enabled by clearing the UCSWRST bit it is ready to receive and transmit
In master mode the bit clock generator is ready, but is not clocked nor producing any clocks.
In slave mode the bit clock generator is disabled and the clock is provided by the master.
A transmit or receive operation is indicated by UCBUSY = 1. The UCBUSY flag is set by writing UCxTXBUF in master mode and in slave mode with UCCKPH=1. In slave mode with UCCKPH=0 UCBUSY is set with the first UCLK edge. UCBUSY is reset by the following conditions:
  In master mode when transfer completed and UCxTXBUF empty.
  In slave mode with UCCKPH=0 when transfer completed.
  In slave mode with UCCKPH=1 when transfer completed and UCxTXBUF empty.
Transmit Enable
  In master mode, writing to UCxTXBUF activates the bit clock generator and the data will begin to transmit.
  In slave mode, transmission begins when a master provides a clock and, in 4-pin mode, when the UCxSTE is in the slave-active state.
Receive Enable
  The SPI receives data when a transmission is active. Receive and transmit operations operate concurrently.

## Slide 58: Serial Clock Control
UCxCLK is provided by the master on the SPI bus
  When UCMST = 1, the bit clock is provided by the USCI bit clock generator on the UCxCLK pin. The clock used to generate the bit clock is selected with the UCSSELx bits.
  When UCMST = 0, the USCI clock is provided on the UCxCLK pin by the master, the bit clock generator is not used, and the UCSSELx bits are don’t care.
The 16-bit value of UCBRx in the bit rate control registers UCxxBR1 and UCxxBR0 is the division factor of the USCI clock source, BRCLK. The maximum bit clock that can be generated in master mode is BRCLK.
Modulation is not used in SPI mode and UCAxMCTL should be cleared when using SPI mode for USCI_A. The UCAxCLK/UCBxCLK frequency is given by F(BRCLK)/UCBRx

## Slide 59: USCI SPI Timing
Polarity and phase of UCxCLK can be controlled by UCCKPH and UCCKPL control bits

## Slide 60: SPI Registers

## Slide 61: SPI Registers (cont’d)

## Slide 64: C Examples, SPI Full-Duplex
//******************************************************************************
// MSP-FET430P140 Demo - USART0, SPI Full-Duplex 3-Wire Slave P1.x Exchange
//
// Description: SPI Master communicates at fast as possible, full-duplex with
// SPI Slave using 3-wire mode. The level on P1.4/5 is TX'ed and RX'ed to P1.0
// and P1.1. Master will pulse slave Reset on init to insure synch start.
// Slave normal mode is LPM4.
// ACLK = n/a, MCLK = SMCLK = DCO ~ 800kHz, ULCK = external
//
// fet140_slav0 fet140_mstr0
// MSP430F169 Slave MSP430F169 Master
// ----------------- -----------------
// | XIN|- /|\| XIN|-
// | | | | |
// | XOUT|- --|RST XOUT|-
// | | /|\ | |
// | RST|--+<----|P3.0 |
// LED <-|P1.0 | | P1.4|<-
// LED <-|P1.1 | | P1.5|<-
// ->|P1.4 | | P1.0|-> LED
// ->|P1.5 | | P1.1|-> LED
// | SIMO0/P3.1|<-------|P3.1 |
// | SOMI0/P3.2|------->|P3.2 |
// | UCLK/P3.3|<-------|P3.3 |
//
// M. Buccini
// Texas Instruments Inc.
// Feb 2005
// Built with IAR Embedded Workbench Version: 3.21A
//******************************************************************************
#include <msp430x14x.h>
void main(void)
{
WDTCTL = WDTPW + WDTHOLD; // Stop watchdog
P1OUT = 0x00; // P1.0 setup for LED output
P1DIR |= 0x03;
P3SEL |= 0x0E; // P3.1,2,3 SPI option select
U0CTL = CHAR + SYNC + SWRST; // 8-bit, SPI
U0TCTL = CKPL + STC; // Polarity, 3-wire
U0BR0 = 0x02; // SPICLK = SMCLK/2
U0BR1 = 0x00;
U0MCTL = 0x00;
ME1 |= USPIE0; // Module enable
U0CTL &= ~SWRST; // SPI enable
IE1 |= URXIE0 + UTXIE0; // RX and TX int. enable
_BIS_SR(LPM4_bits + GIE); // Enter LPM4 w/ int.
}
#pragma vector=USART0RX_VECTOR
__interrupt void SPI0_rx (void) {
P1OUT = RXBUF0; // RXBUF0 to TXBUF0
}
#pragma vector=USART0TX_VECTOR
__interrupt void SPI0_tx (void) {
unsigned int i;
i = P1IN;
i = i >> 4;
TXBUF0 = i; // Transmit character
}

## Slide 65: CPE 323 Introduction to Embedded Computer Systems: The MSP430 I2C
Instructor: Dr Aleksandar Milenkovic Lecture Notes

## Slide 66: I2C: Inter-Integrated Circuit Bus
I2C – introduced by Philips (NXP) Semiconductors
  a.k.a. two-wire interface
True bus, with well-defined specification
Two bidirectional lines
  SDA: Serial Data
  SCL: Serial Clock
More complex than SPI, more HW resources (e.g., in USCI_B), slower than SPI

## Slide 67: I2C Operation
Each I2C device is recognized by a unique address and can operate as either a transmitter or a receiver.
A device connected to the I2C bus can be considered as the master or the slave when performing data transfers
  A master initiates a data transfer and generates the clock signal SCL.
  Any device addressed by a master is considered a slave.
I2C uses two bidirectional lines connected to a positive supply voltage through a pullup transistor (wired-and)
  Serial data pin (SDA)
  Serial clock pin (SCL)

## Slide 68: I2C Serial Transfer
One clock pulse is generated by the master device for each data bit transferred. The I2C mode operates with byte data. Data is transferred most significant bit first.
The first byte after a START condition consists of a 7-bit slave address and the R/#W bit
  When R/#W = 0, the master transmits data to a slave.
  When R/#W = 1, the master receives data from a slave.
The ACK bit is sent from the receiver after each byte on the 9th SCL clock.

## Slide 69: I2C Serial Transfer (cont’d)
START and STOP conditions are generated by the master
A START condition is a high-to-low transition on the SDA line while SCL is high.
A STOP condition is a low-to-high transition on the SDA line while SCL is high.
The bus busy bit, UCBBUSY, is set after a START and cleared after a STOP.
Data on SDA must be stable during the high period of SCL
  The high and low state of SDA can only change when SCL is low, otherwise START or STOP conditions will be generated.

## Slide 70: Hardware for I2C

## Slide 71: Master Reads from a Slave

## Slide 72: I2C Addressing Modes

## Slide 73: Slave Transmitter Mode
Slave transmitter mode is entered when the slave address transmitted by the master is identical to its own address with a set R/W bit (read).
The USCI module is automatically configured as a transmitter and UCTR and UCBxTXIFG become set
  The slave transmitter shifts the serial data out on SDA with the clock pulses that are generated by the master device
The slave device does not generate the clock, but it will hold SCL low while intervention of the CPU is required after a byte has been transmitted.
The SCL line is held low until the first data to be sent is written into the transmit buffer UCBxTXBUF. Then the address is acknowledged, the UCSTTIFG flag is cleared, and the data is transmitted.

## Slide 74: Slave Transmitter Mode (cont’d)
The SCL line is held low until the first data to be sent is written into the transmit buffer UCBxTXBUF. Then the address is acknowledged, the UCSTTIFG flag is cleared, and the data is transmitted.
As soon as the data is transferred into the shift register the UCBxTXIFG is set again. After the data is acknowledged by the master the next data byte written into UCBxTXBUF is transmitted or if the buffer is empty the bus is stalled during the acknowledge cycle by holding SCL low until new data is written into UCBxTXBUF.
If the master sends a NACK succeeded by a STOP condition the UCSTPIFG flag is set. If the NACK is succeeded by a repeated START condition the USCI I2C state machine returns to its address-reception state.

## Slide 75: Slave Transmitter Mode

## Slide 76: Slave Receiver Mode
Slave receiver mode is entered when the slave address transmitted by the master is identical to its own address and a cleared R/#W bit is received.
The USCI module is automatically configured as a receiver and UCTR is cleared. After the first data byte is received the receive interrupt flag UCBxRXIFG is set.
Serial data bits received on SDA are shifted in with the clock pulses that are generated by the master device
  The slave device does not generate the clock, but it can hold SCL low if intervention of the CPU is required after a byte has been received.
The USCI module automatically acknowledges the received data and can receive the next data byte.
If the previous data was not read from the receive buffer UCBxRXBUF at the end of a reception, the bus is stalled by holding SCL low. As soon as UCBxRXBUF is read the new data is transferred into UCBxRXBUF, an acknowledge is sent to the master, and the next data can be received.

## Slide 77: Slave Receiver Mode (cont’d)
Setting the UCTXNACK bit causes a NACK to be transmitted to the master during the next acknowledgment cycle. A NACK is sent even if UCBxRXBUF is not ready to receive the latest data.
If the UCTXNACK bit is set while SCL is held low the bus will be released, a NACK is transmitted immediately, and UCBxRXBUF is loaded with the last received data.
Since the previous data was not read that data will be lost. To avoid loss of data the UCBxRXBUF needs to be read before UCTXNACK is set.
When the master generates a STOP condition the UCSTPIFG flag is set.
If the master generates a repeated START condition the USCI I2C state machine returns to its address reception state.

## Slide 78: Slave Receiver Mode