## Slide 1: CPE 431/531 Chapter 2 – Instructions: Language of the Computer
Dr. Rhonda Kay Gaede

## Slide 2: 2.1 Introduction
The words of a computer’s language are called _________ and its vocabulary is called an ________ ___ ________________.
Instruction sets are more similar than they are different, however there are two camps:
  RISC – _____________
  CISC – ________

## Slide 3: 2.2 Basics of MIPS Arithmetic
We need arithmetic
  add a, b, c
From high level
  a = b + c + d + e;
________ the number of operands keeps the hardware _______.
Design Principle 1: Simplicity favors regularity
Notes: Add a, b, c
Add a, a, d
Add a, a, e

## Slide 4: 2.2 Compiling C into MIPS
Compilation is the process of creating MIPS assembly language from a high level language.
Examples:
  a = b + c;
  d = a – e;
  f = (g + h) – (i + j);
Notes: a = b + c; add a, b, c
d = a – e; sub d, a, e
f = (g + h) – (i + j); (1) add t0, g, h
add t1, i, j
sub f, t0, t1
(2) add t0, g, h
sub t0, t0, i
sub t0, t0, j

## Slide 5: 2.3 MIPS Basics
In high level languages, variables live in _________
In MIPS assembly, operands live only in ___________
_____________ instructions move variables from memory/registers to registers/memory.
MIPS has ___ registers and an address space of ____ memory bytes.
Design Principle 2: Smaller is faster.
Notes: Decoding takes longer when the number of registers increases. Also, more registers means that instruction fields must be larger.

## Slide 6: 2.2 Compiling C into MIPS (Registers)
Reconsider
  f = (g + h) – (i + j);
  The variables f, g, h, i, and j are assigned to registers $s0, $s1, $s2, $s3, and $s4, respectively.
Notes: f = (g + h) – (i + j); (1) add $t0, $s1, $s2
add $t1, $s3, $s4
sub $s0, $t0, $t1
(2) add $t0, $s1, $s2
sub $t0, $t0, $s3
sub $t0, $t0, $s4

## Slide 7: 2.3 Memory Operands: First Pass
Data transfer instructions
  Load
  Store
Compiling an Assignment When an Operand is in Memory
  The compiler has associated g with $s1 and h with $s2 and A is an array of 100 words, base pointer $s3
  g = h + A[8];
Hardware/Software Interface
  A compiler translates, associates variables with registers, allocates memory to data structures.
Notes: G = h + A[8]; lw $t0, 8($s3)
add $s1, $s2, $t0

## Slide 8: 2.3 Memory Operands: Second Pass
Bytes/Words
  32-bit words consist of 4 8-bit bytes
  Computers are bigendian or little endian depending on whether the _____ _____ is _____ or _____ significant
  MIPS is _____ addressable
Compiling Using Load and Store
h is associated with $s2 and the base address of A is in $s3
  A[12] = h + A[8];
. Hardware/Software Interface
  The compiler keeps frequently used items in registers, spills other variables to memory.
Notes:   lw $t0, 32($s3)
  add $t0, $t0, $s2
  sw $t0, 48($s3)

## Slide 9: 2.3 Constant or Immediate Operands
More than half of the MIPS arithmetic instructions have a ________ as an operand when running the SPEC CPU 2006 benchmarks.
With the instructions we’ve seen so far, constants must be put in ________ when the program was loaded and then we would have to load them into a _______ to use.
The alternative is to add a different kind of instruction.
  addi $s3, $s3,4
Design Principle 3: Make the common case fast.

## Slide 10: 2.4 Signed and Unsigned Numbers
Unsigned
  10112 =
  Range for n bits:
Signed
  10112 =
  Range for n bits:
Finding the 2’s complement
  00001010
  00101000
Sign Extension
  00001010
  10110111

## Slide 11: 2.5 R-type Instruction Format
Translating a MIPS assembly instruction into a machine instruction:
add $t0, $s1, $s2 (R-type)
    Op(6) rs(5) rt(5) rd(5) shamt(5) funct(6)
MIPS Fields
op: opcode
rd: register destination
rs: first register source
rt: second register source/destination register for lw shamt: shift amount
funct: function code

## Slide 12: 2.5 I-Type Instruction Format
One size doesn’t fit all. lw and sw have different requirements than add.
Design Principle 4: Good design demands good compromises.
lw $t0, 32($s3)
op(6) rs(5) rt(5) constant or address(16)
For data transfer, address offset is limited to ________, _________.
Another Translation Example: A[300] = h + A[300];
Notes:   lw $t0, 1200($t1) 35 9 8 1200
  add $t0, $s2, $t0 0 18 8 8 0 32
  sw $t0, 1200($t1) 43 9 8 1200

## Slide 13: 2.5 Instructions for Making Decisions
Two conditional ones for now:
  beq register1, register2, L1
  bne register1, register2, L1
  if (i == j)
    f = g + h;
  else
    f = g – h;
Notes: bne $s3, $s4, Else beq $s3, $s4, Then
add $s0, $s1, $s2 sub $s0, $s1, $s2
j Exit j Exit
Else: sub $s0, $s1, $s2 Then: add $s0, $s1, $s2
Exit: Exit:

## Slide 14: 2.7 Adding less than or greater than
Less than is useful, i.e., for (i = 0; i < 10; i++)
  slti $t0, $s1, 10
bne $t0, $zero, offset
slt $t0, $s0, $s1
bne $t0, $zero, offset
Notes: slti and bne together make blti
if ($s1 < 10) then
$t0  1
else
$t0  0
If ($t0 != 0) then
PC  PC + 4 + offset << 2
Else
PC  PC + 4
slt and bne together make blt

## Slide 15: 2.7 Compiling a while loop
Consider
while (save[i] == k)
i++;
where is associated with $s3 and k with $s5 and the base of array save is $s6.
Notes: Loop: sll $t1, $s3, 2
add $t1, $t1, $s6
lw $t0, 0($t1)
bne $t0, $s5, Exit
addi $s3, $s3, 1
j Loop
Exit:

## Slide 16: 2.8 Supporting Procedures in Computer Hardware
Steps involved in calling a procedure (function)
    Make ___________ available to the ______ procedure
    Transfer ________ to the procedure
    _________ the needed _______ for the procedure.
    Perform the ________ ____
    Make ______ ________ to the calling procedure
    Transfer ________ back to _______ procedure
Support comes in registers and instructions
  Registers
    $a0-$a3 –
    $v0-$v1 –
    $ra
  Instructions
    jal,
    jr
Notes: jal Procedure Address
$ra  PC + 4
PC  Procedure Address
jr $ra
PC  $ra
As long as the input parameters fit in 128 bits and the results fit in 64 bits, you don’t need anything else. However, we often need more, spill them to the stack. $sp points to the last used space.

## Slide 17: 2.8 Compiling a Leaf Procedure
int leaf_example (int g, int h, int i, int j)
{
  int f;
  f = (g + h) - (i + j);
  return(f);
}
leaf_example: sub $sp, $sp, 12
sw $t1, 8($sp)
sw $t0, 4($sp)
sw $s0, 0($sp)
add $t0, $a0, $a1
add $t1, $a2, $a3
sub $s0, $t0, $t1
add $v0, $s0, $Zero
lw $s0, 0($sp)
lw $t0, 4($sp)
lw $t1, 8($sp)
add $sp, $sp, 12
jr $ra
Notes: Look at ways to streamline. First, don’t save temporary registers. If not saved, don’t need to be restored. Make sure you adjust the stack pointer accordingly. Could also make $v0 the destination of the sub and get rid of add $b0, $s0, $zero. MIPS has a callee save convention.

## Slide 18: 2.8 Leaf Example Stack
In the previous example, what happens if we change the procedure to have one more argument? _Spill them to the stack_

## Slide 19: 2.8 Nested Procedures
Calling Procedure
  Pushes its argument registers onto the stack so it can put arguments there for the callee
  Pushes any temporary registers it needs after the call onto the stack
  Pushes $ra onto the stack
Called Procedure
  Pushes saved registers it plans to use onto the stack

## Slide 20: 2.8 Nested Procedure Compilation
int fact (int n)
{
  if (n < 1) return (1);
  else return (fact(n*n-1));
}
fact: addi $sp, $sp, -8
sw $ra, 4($sp)
sw $a0, 0($sp)
slti $t0, $a0, 1
beq $t0, $zero, L1
addi $v0, $zero, 1
addi $sp, $sp, 8
jr $ra
L1: addi $a0, $a0, -1
jal fact
lw $a0, 0($sp)
lw $ra, 4($sp)
addi $sp, $sp, 8
mul $v0, $a0, $v0
jr $ra
Notes: You may not make another call but you must be prepared if you do, so store $ra, last time wasted.

## Slide 21: 2.8 More About the Stack
Allocating Space for Automatic Variables
  In addition to storing saved registers, the stack holds local variables that don’t fit into registers, e.g., arrays, structs.
  Saved registers + Local Variables = Procedure Frame
Notes: $fp doesn’t change during procedure. Reference saved items through $fp. A – before the call, b – during the call, c - after the call.
The stack pointer may change during the procedure but the frame pointer doesn’t.

## Slide 22: 2.8 The Heap
Space is needed for ______ variables and _______ data structures
  Space is reserved and freed on the heap using ________ ______ ______.
Register Usage
  $zero 0
  $v0-$v1 2-3
  $a0-$a3 4-7
  $t0-$t7 8-15
  $s0-$s7 16-23
  $t8-$t9 24-25
  $gp 28
  $sp 29
  $fp 30
  $ra 31
Notes: $gp is the global pointer that points to the static area. By having the stack grow down in the memory and the heap grow up in memory, hopefully they don’t intersect.

## Slide 23: 2.10 32-bit Immediate Operands
32-Bit Immediate Operands
  Upper 16 Bits - lui
  Lower 16 Bits - ori
Loading 0x003D 0900
Notes: Loading 32 bit operands is a two step process. Lui $s0, 61, ori $s0, $s0, 2304. Why not addi? Sign extension

## Slide 24: 2.10 32-Bit Addresses
Addresses in Branches and Jumps
  j 10000
  bne $s0, $s1, Exit
  Elaboration: For jumps, we give only 28 bits, from whence springeth the other 4?
  Branching Far Away
Notes: We can branch only 216 words away. This is PC-relative addressing. We could specify bytes but that would be wasting two bits since addresses are word aligned. We get the other two bits from PC + 4.
Branching far away.
bne $s0, $s1, L2
j L1
L2:

## Slide 25: 2.11 Parallelism and Instructions: Synchronization
Cooperation between tasks usually means some tasks are ________ new values that others must ____
In computing, synchronization mechanisms are typically built with ___________ software routines that rely on _________-supplied synchronization instructions
One hardware primitive will both read from and write to a location in one ________ operation
The other approach is to have a ___ of instructions in which the ________ instruction _______ __ _______ showing whether the pair of instructions was executed as if the pair were atomic
MIPS has _____ ______, __, and _____ _____________, __

## Slide 26: 2.11 Code Sequence for Atomic Exchange
    again: addi $t0,$zero,1 ;copy locked value
    ll $t1,0($s1) ;load linked
    sc $t0,0($s1) ;store conditional
    beq $t0,$zero,again ;branch if store fails
    add $s4,$zero,$t1 ;put load value in $s4
Notes: $t0  1
$t1  Mem[$s1+0]
Mem[$s1+0]  $t0, if Mem[$s1+0] hasn’t changed, $t0  1 (this processor has the lock)
else $t0  0
All that’s happening here is the variable is read without corruption. Exchange (might be two way, might be one way) might be a misnomer. Most of the time, you want to ll, do some stuff, then sc.

## Slide 27: 2.12 Translating and Starting a Program

## Slide 28: 2.20 Fallacies and Pitfalls
Fallacy: More powerful instructions mean higher performance.
Fallacy: Write in assembly language to obtain the highest performance.
Fallacy: The importance of commercial binary compatibility means successful instruction sets don’t change.
Pitfall: Forgetting that sequential word addresses in machines with byte addressing do not differ by one.
Pitfall: Using a pointer to an automatic variable outside its defining procedure.
Notes: Making a really powerful instruction can slow all instructions down. Powerful instructions might be long, requiring multiple expensive memory accesses.
Problems arise from lack of portability and the cost of maintaining assembly.
The x86 instruction set has added more than one instruction per month over a life of 35 years.
Pointing to the stack is a problem, the stack gets reused.