## Slide 1: Consider a 64KB direct mapped cache with 128 word blocks. How many index bits are there? Only word addresses are used and a word is 64 bits. Addresses are 32-bits.
5
6
7
8
9
10
Don‘t Know

## Slide 2: Consider a 64KB direct mapped cache with 128 word blocks. How many block offset bits are there? Only word addresses are used and a word is 64 bits. Addresses are 32 bits.
5
6
7
8
9
10
Don’t Know

## Slide 3: Consider a 64KB direct mapped cache with 128 word blocks. How many tag bits are there? Only word addresses are used and a word is 64 bits. Addresses are 32-bits.
3
7
13
17
19
21
Don’t Know

## Slide 4: Consider a 64KB 8-way set associative cache with 32 word blocks. How many index bits are there? Only word addresses are used and a word is 64 bits. Addresses are 32 bits.
5
6
7
8
9
10
Don’t Know

## Slide 5: Consider a 64KB 8-way set associative cache with 32word blocks. How many block offset bits are there? Only word addresses are used and a word is 64 bits. Addresses are 32 bits.
5
6
7
8
9
10
Don’t Know

## Slide 6: Consider a 64KB 8-way set associative mapped cache with 32 word blocks. How many tag bits are there? Only word addresses are used and a word is 64 bits. Addresses are 32-bits.
5
9
16
18
22
25
Don’t Know

## Slide 7: Consider a 1024 word 2-way set associative mapped cache with 32 word blocks. Only word addresses are used. What set does the word address 27,435 map to?
3
5
8
9
10
25
Don’t Know

## Slide 8: Consider a 1024 word 2-way set associative mapped cache with 32 word blocks. Only word addresses are used. What are the word addresses of the data brought in when a data item at address 27,435 is read from main memory?
27,424 – 27,455
27,435 - 27,466
27,435 – 27,451
27,424 – 27,439
Don’t Know

## Slide 9: Instruction cache miss rate of 4%, data cache miss rate of 10%, Base CPI = 1.0 (no data or control hazards), 20% of instructions are loads and stores, miss penalty = 12 cycles, CPI = ?
1.241
1.34
1.48
1.72
None of the above